## Slide 1
Project 3 Pin Diagram – LCD Slave
MSP430
Launchpad ..
Keypad
C2
C3
C4
R1
P5.3
P5.1
P5.0
P5.4
GND
VCC
5V
C1
P1.4
R2
P1.1
R3
P3.5
R4
P3.1
P1.2
P1.3
SDA
SCL

## Slide 2
Project 4 Pin Diagram – LED Slave
MSP430
FR2311
GND
VCC
5V
P1.0
P2.7
P2.6
P1.4
P1.1
P1.5
Led 1
P2.0
P1.2
P1.3
SDA
SCL
P1.6
P1.7

## Slide 3
Project 5 Pin Diagram – LCD Slave
MSP430
LCD
R/W
DB7
DB6
DB5
P2.1
P2.2
P6.0
P6.1
GND
VCC
5V
R/S
P2.0
DB4
P6.2
DB3
P6.3
DB1
P6.4
P6.4
DB0
P1.2
P1.3
SDA
SCL

## Slide 4
Init
Keypad
  Columns as outputs on P1.4, 5.3, 5.1, 5.0
  Rows pulled low on P5.4, 1.1, 3.5, 3.1
ADC
  12-bit conversion using A10 on P5.2
  TB3 at 4.096 Hz with CCR set to 2047 (.5s)
I2C Master
  SDA (P1.2), SCL (P1.3) with autostop at 100 kHz
Clear LCD with standard message
Turn LED bar off
Main
Project 4 Flowchart - Main
Wrong
Set Variables:
(A to set pattern)
(B to set window size)
(C to toggle C/F units)
(* to exit either mode)
Update RGB Status Led
Wait for passcode
Correct
Read Keypad
If D
SAMPLING ISR ON TB3:
Enqueue new ADC value to array holding values for the windowed average
Dequeue last value
Update average by comparing enqueued and dequeued values
If the array is filled, send average to LCD
Start next ADC read
Clear CCR flag

## Slide 5
Init
Heartbeat on P2.0
Initialize LED 1-8 as outputs on P1.1, P1.0, P2.7, P2.6, P1.4, P1.5, P1.6, P1.7 respectively
Initialize vars for pattern display (patterns, vars for iterating through and pattern memory)
Timer for displaying patterns on TB1
I2C slave operation
Main
Project 4 Flowchart – LED Bar
Set delay fast
Toggle Heartbeat LED
Wait for DELAY
Is I2C RX triggered?
Set delay slow
True
False
RX ISR:
Read in integer
Update previous pattern and associated state
Update pattern and state to be displayed
Set delay fast

## Slide 6
Init
I2C slave operation
LCD initialization (pins,8-bit mode, cursor mode)
Main
Project 4 Flowchart – LCD Disp.
RX ISR:
Read all characters
Clear LCD
Write message to LCD

## Slide 7
Project 3: Main Controller
KEYPAD
GPIO
I2C Bus
Slave MSP430s

## Slide 8
Project 3: LED Bar
RGB Patterns
LED Light Bar
TIMER
GPIO
I2C Bus
Master MSP430

## Slide 9
Project 3: LCD Display
RGB Patterns
LCD Display
TIMER
GPIO
I2C Bus
Master MSP430